## Slide 1
DGIST
Flash-based SSDs
Presenter:
Daehan Lee

## Slide 2: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 3: Introduction
A new form of persistent storage device has recently gained signiﬁcance in the world. Generically referred to as solid-state storage, such devices have no mechanical or moving parts like hard drives.
Typical random-access memory (e.g., DRAM), such a solid-state storage device (a.k.a., an SSD) retains information despite power loss, and thus is an ideal candidate for use in persistent storage of data.
The technology we’ll focus on is known as ﬂash (NAND-based ﬂash), which was created by Fujio Masuoka in the 1980s
Interesting challenge
  You first have to erase a bigger chunk(a block), if you want to write to a given chunk of it (a page)
  Writing too often to a page will cause it to wear out
DGIST
Notes: SSD와 HHD의 차이에 대해 설명
Mechanical한 장치나 moving parts ex. 헤더 같은 부분이 없음.
전자적인 방식으로 구성되었기때문에 비교적 내구성이 좋음. DRAM과 같은 전형적인 랜덤 엑세스 메모리처럼 작동하나 전력이 없을때도 데이터 손실이 일어나지 않음.
이 flash-based SSDs의 경우 두가지의 문제점이 있는데
Page를 쓰기 위해서는 반드시 하나의 큰 block을 지워야함
Wear out 닳는 다는 문제가 생김

## Slide 4: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 5: Storing a Single Bit, From Bits to Banks/Planes
Flash chips are designed to store one or more bits in a single transistor
  SLC (single-level cell) - You can only store a single bit within transistor
  MLC (multi-level cell) - Two bits are encoded into different levels of charge. 00,01,10 and 11
  TLC (triple-level cell) - Three bits are encoded into different levels of charge.
A bank is accessed in two different sized units
  Blocks (sometimes called erase blocks), which are typically of size 128 KB or 256 KB
  pages, which are a few KB in size (e.g., 4KB)
  Within each bank there are a large number of blocks and within each block, there are a large number of pages.
  The most important (and weird) thing you will learn is that to write to a page within a block, you ﬁrst have to erase the entire block
  CF. The terms that are written in this part are different than the blocks we refer to in disks and RAID structure and the pages we refer to in virtual memory
DGIST
Notes: 하나의 플래시 칩을 만들 때 몇 개의 bit를 넣느냐애 따라 성능과 신뢰성이 달라짐.
SLC, MLC TLC는 각각 1개,2개,3개의 비트를 트렌지스터에 넣어 사용함. 성능과 신뢰성 측면에서는 이후에 더 살펴봄
Page는 비교적 작은 데이터 크기를 가지고 있고 block은 이보다 더 큰 데이터 크기를 차지하고 있음.
즉 여러 개의 page가 모여서 여러 개의 block이 되고 이 block이 여러 개 모이면 bank를 구성함.
다시 말하듯 가장 중요한 것은 block 안에 있는 page를 쓰기 위해서는 반드시 block 단위의 erase 작업이 필요함

## Slide 6: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 7: Basic Flash Operations
There are three low-level operations that a ﬂash chip supports
  Read (a page)
    Can read any page (e.g., 2KB or 4KB).
    Typically quite fast regardless of location on the device.
    Being able to access any location uniformly quickly means the device is a random access device.
  Erase (a block)
    Before writing to a page within a ﬂash, the nature of the device requires that you ﬁrst erase the entire block the page lies within.
    Before executing the erase, you must be sure that important data has been copied elsewhere
    Once ﬁnished, the entire block is reset and each page is ready to be programmed.
  Program (a page)
    Programming a page is less expensive than erasing a block
    but more costly than reading a page
DGIST
Notes: Flash에서는 총 3가지의 low-level operatio이 있음.
첫 번째는 read, 그다음은 erase, 그리고 program임.
Read는 이 3가지중에서 가장 쉽고 가벼운 연산으로 어느 페이지나 읽을수 있으며 가장 빠른 속도를 가지고 있음. Random access를 의미
Erase는 여기서 가장 값 비싼 연산임. 이 연산을 해야 비로소 program할 준비가 되어있음. 여러 번 말했듯 page 단위의 write를 수행하기 위해 반드시 block 단위의 erase 작업이 필요함. Page 단위로 쓰기 위해 블록을 전부 지워야하니 당연히 중요한 데이터들은 백업을 할 필요가 있음.
Program은 earse에 비하면 양반. 하지만 read보다는 비쌈

## Slide 8: Basic Flash Operations (cont.)
One way to think about ﬂash chips
  Each page has a state associated with it.
  Pages start in an INVALID state.
  Set the state of the page to ERASED, which resets the content of each page in the block but also makes them programmable.
  When you program a page, its state changes to VALID, meaning its contents have been set and can be read.
DGIST
Notes: 이제 예시를 한번 보자
처음에는 invalid한 상황. 우리는 무언가 쓰고 싶음.
그러면 앞에서 여러 번 말한 것처럼, 해당 블록 전체를 다 지워야할 필요가 있음. 그래서 erase 작업이 이뤄지고 page 0에 뭔가를 쓸 준비가 되었음. 정상적으로 씀. 이제 이 page 0에 있는 무언가를 수정하고 싶으나 erase가 안됐기 때문에 불가함
Program1번의 경우 erase된 상황이니 write가 가능

## Slide 9: Basic Flash Operations (cont.)
A Detailed Example
  imagine we have the following four 8-bit pages, within a 4-page block
  We wish to write to page 0, filling it with new contents. To write any page, we must ﬁrst erase the entire block.
  Go ahead and program page 0, with the contents 00000011, overwriting the old page 0 (contents 00011000).
DGIST
Notes: 디테일한 예시를 들며 설명
Page 하나당 8bit를 담을 수 있고 4개의 page가 있다고 가정.
우리는 page 0번에 뭘 쓰고 싶음. 여러 번 말했듯 이 블록 전체를 다 지워야함 먼저.
지우고 page 0에 드디어 뭘 썼음

## Slide 10: Basic Flash Operations (cont.)
A Detailed Example (cont.)
  But the previous contents of pages 1, 2, and 3 are all gone.
  Thus, before overwriting any page within a block, ﬁrst move any data we care about to another location
  And this erased characteristic has a lot to do with the design of Flash-based SSE.
Summary
  Reading a page is easy
    just read the page
  Writing a page is trickier
    Not only is this expensive, but frequent repetitions can lead to “wear out”
  The performance and reliability of writing is a central focus
    Soon learn more about how modern SSDs attack these issues
DGIST
Notes: 근데 이제 문제가 1,2,3이 다 사라졌음..
블록안에 뭔가를 overwriting 하기전에 데이터를 반드시 먼저 써야함
Ok 지금까지 요약하면
읽기는 쉬움.
Write는 까다로움 비용의 문제뿐만 아니라 wear out이라는 신뢰성에 영향을 주는 요소를 가지고 있기 때문.

## Slide 11: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 12: Flash Performance And Reliability
Performance of SLC , MLC and TLC flash
  Read latencies are quite good
  Program latency is higher and more variable for SLC. But higher as you pack more bits into each cell
    To get good write performance, have to make use of multiple flash chips in parallel
  Erases are quite expensive, so Dealing with this cost is central to modern flash storage design
DGIST
Notes: 아까 말했듯 한 트랜지스터에 몇 개의 비트를 넣어 플래시칩을 설계하느냐에 따라서 퍼포먼스와 신뢰도측면에서 다른 결과를 보임.
모든 경우 READ에서는 꽤 좋은 모습을 보이나, WRTIE에서는 비교적 높은 latency를 보임. 이는 더 많은 비트를 포함할 수록 latenc가 증가하는 것을 볼 수 있음. Write 퍼포먼스를 증가시키기 위해서는 플래시 칩들을 병렬적으로 작용할 수 있도록 설계해야함.
Erase의 경우 가장 비산 연산이다.

## Slide 13: Flash Performance And Reliability (cont.)
Reliability of flash chips
  Flash chips aren’t mechanical disks, these are pure silicon and in that sense have fewer reliability issues to worry about like physical head crush
  The primary concern is “wear out”; when a ﬂash block is erased and programmed, it slowly accrues a little bit of extra charge
  Lifetime (currently not well known)
    SLC based block - 100,000 P/E
    MLC based block - 10,000 P/E
    Recent research has shown that lifetimes are much longer than expected
  Disturbance
    it is possible that some bits get ﬂipped in neighboring pages; such bit ﬂips are known as read disturbs or program disturbs
DGIST
Notes: 플래시 칩은 기계적인 요소로 이루어진 것이 아니다 보니 외부적인 충격에 의해서는 상당히 좋은 신뢰도를 줄 수 있음.
하지만 wear out이라는 문제점을 가지고 있는데, 정확히 알려진 것은 아니지만 SLC, MLC 각각 이정도의 라이프 타임을 가지고 있음.
Wear out이란 우리가 종이를 썼다가 지우면 종이가 너덜거리는 것과 같은 원리.
Distrubance란 플래시 칩이 전자적인 요소로 설계되었기 때문에 나오는 문제점이다. 우리가 컴퓨터를 사용하면 으레 그렇듯 자주 사용하는 것만 사용하게 된다. 이렇게 되면 특정 page에 반복적인 전압이 가해지고 이렇게 되면 주변 page들의 bit flip되는 현상이 일어남.

## Slide 14: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 15: From Raw Flash to Flash-Based SSDs
How to turn a basic set of ﬂash chips into something that looks like a typical storage device
  The standard storage interface is a simple block based one, where blocks (sectors) of size 512 bytes (or larger) can be read or written, given a block address
  The task of the ﬂash-based SSD is to provide that standard block interface atop the raw ﬂash chips inside it.
An SSD consists of some number of ﬂash chips and also contains some amount of volatile memory
DGIST
Notes: 지금까지는 플래시 칩에 대해 이야기 했으니 이거를 어떻게 우리가 알고 있는 저장장치처럼 보이게 할 것인가에 대한 장.
다시 말해, flash based SSD의 업무중 하나는 표준 블록 인터페이스를 제공하는 것이다.
보이는 것처럼 ssd는 플래시 칩도 있지만 휘발성 메모리를 두는데 이런 메모리는 캐시와 같은 역할에 사용된다.

## Slide 16: From Raw Flash to Flash-Based SSDs (cont.)
FTL(Flash Translation Layer)
  Read and write requests on logical blocks
  Turns them into low-level read, erase, and program commands on the underlying physical blocks and physical pages
  Accomplish this task with the goal of delivering excellent performance and high reliability
  Wear leveling - Should try to spread writes across the blocks of the ﬂash as evenly as possible, ensuring that all of the blocks of the device wear out at roughly the same time
  To minimize disturbance - commonly program pages within an erased block in order, from low page to high page
DGIST
Notes: FTL이란 SSD의 작동을 컨트롤 하기 위한 자료구조같은 개념으로, logical block에서 읽기 쓰기 요청을 가져와서 low-level의 flash operation들로 변환하여 수행하는 역할을 한다.
또한 wear leveling이라는 작업을 수행하는데 메모리가 균등하게 사용되어 최대한 특정 플래시의 마모를 막는 역할을 한다.
그리고 page에 대해 program operation이 실행될 때 낮은 번호부터 높은 번호로 매핑을 하여 최대한의 disturbance를 줄인다.

## Slide 17: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 18: FTL Organization: A Bad Approach
Direct mapped
  The simplest organization
  A read to logical page N is mapped directly to a read of physical page N
  But A write to logical page N is more complicated
    First it has to read in the entire block that page N is contained within
    Then it has to erase the block
    Finally it programs the old pages as well as the new one
  Direct mapped FTL has many problem in terms of performance as well as reliability
    Performance
      Have to read in the entire block (costly). erase it (quite costly). program it (costly).
      The end result is severe write ampliﬁcation
      Even slower than typical hard drives
DGIST
Notes: FTL에 대해 자세하게 보자.
FLT을 생각할때 우리가 가장 먼저 떠올릴 수 있는 방법은 direc하게 mappe하는 방법이다. 논리적 page N에 대한 작업을 하기 위해 물리적 page N에 직접 매핑하는 것인데, 가장 간단한 구조이다.
읽기는 위에 설명한 대로 직접 매핑 방식으로 접근하여 읽으면 된다. 쓰기의 경우에는 쓸 page N에 대해 읽고, 그 블록을 지운후에 이전 페이지와 새로운 페이지를 프로그래밍 한다.
이 방식은 성능과 신뢰도 측면에서 좋지 않다.
가장 먼저 성능 면에서는, 전체 블록을 읽어야 하고, 또 지워야하고 다시 써야한다. 이는 페이지 하나를 쓰기 위해서 블록 전체를 다 지워야한다. 불필요한 쓰기 작업을 유도하고 결과적으로 write amplication을 유발한다.

## Slide 19: FTL Organization: A Bad Approach (cont.)
Direct mapped
  Direct mapped FTL has many problem in terms of performance as well as reliability
    reliability
      The direct mapped approach simply gives too much control over wear out to the client workload
      The underlying physical blocks containing popular data will quickly wear out.
For both reliability and performance reasons, a direct-mapped FTL is a bad idea.
DGIST
Notes: 신뢰도 면에서도 좋지 않은 성능을 보임.
Client에게 너무 의존적이기 때문에 특정 work load에 작업량이 몰린다면 이는 wear out을 앞당기는 결과를 가져옴.

## Slide 20: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 21: A Log-Structured FTL
Log structured
  Most FTL Organization
  The device appends the write to the next free spot in the currently-being-written-to block
  The device keeps a mapping table which stores the physical address of each logical block in the system.
Let’s see
  The device looks like a typical disk, in which it can read and write 512-byte sectors
  Assume that the client is reading or writing 4-KB sized chunks
  SSD contains some large number of 16-KB sized blocks
  Divided into four 4-KB pages
DGIST
Notes: 그래서 생각해낸 FTL 구조가 Log-structured FTL 구조임.
이는 블록을 지우지 않고 쓰여진 블록 바로 옆에 있는 free 블록에 붙여서 씀.
직접 1:1로 mapping을 하는 것이 아니기 떄문에, logical과 physical 주소의 정보를 저장하고 있을 mapping table이 필요함.
예를 한번 들어보자.
우리는 512 바이트 섹터를 읽고 쓸수 있는 SSD가 있다고 가정.
이때 4KB 크기의 청크를 수정할 수 있으며, 한 블록의 크기는 16KB, 페이지는 총 4개로 각 페이지의 크기는 4KB임

## Slide 22: A Log-Structured FTL (cont.)
Let’s see
  Write(100) with contents a1
  Write(101) with contents a2
  Write(2000) with contents b1
  Write(2001) with contents b2
  These logical block addresses (e.g., 100) are used by the client of the SSD
  Assume that all blocks of the SSD are currently not valid
  And must be erased before any page can be programme
Here we show the initial state of our SSD, with all pages marked INVALID (i):
DGIST
Notes: 이제 우리가 원하는건 logical 100에 al을 작성하고, a2는 logical 101 이하 같은 방법으로 작동함.
이때 기억해야할건 기존의 SSD page들이 invalid한 상태라는 것. 그렇기때문에 programe되기 전에 당연히 erase해야함.
초기 상태는 전부 invalid니까 state가 다 i로 되어있음

## Slide 23: A Log-Structured FTL (cont.)
When the ﬁrst write is received by the SSD to logical block 100, FTL decides to write it to physical block 0, which contains four physical pages 0, 1, 2, and 3
The block is not erased so we cannot write to it yet
the device must ﬁrst issue an erase command to block 0. Doing so leads to the following state:
Block 0 is now ready to be programmed. Most SSDs will write pages in order (i.e., low to high), reducing reliability problems related to program disturbance.
The SSD then directs the write of logical block 100 into physical page 0:
DGIST
Notes: 이제 logical block 100에 a1을 쓰고 싶어함. 그러면 당연히 이 블록을 먼저 지워야함. 그래서 블록 0번을 지우고 state는 다음과 같이 변함. 이제 program 될 준비가 되었으니
Page 0번에 a1을 기입함. 이때 page를 기입하는 순서는 낮은 순서부터 높은 순서로 올라가는데 앞에 배웠던 것 처럼 disturbanc를 방지하기 위함임.

## Slide 24: A Log-Structured FTL (cont.)
But what if the client wants to read logical block 100?
When the FTL writes logical block 100 to physical page 0, it records this fact in an in-memory mapping table.
We will track the state of this mapping table in the diagrams as well:
What happens when the client write to the SSD.
  Finds a location for the write, usually just picking the next free page
  Then programs that page with the block’s contents
  And records the logical-to-physical mapping in its mapping table
DGIST
Notes: 하지만 만약에 방금 직전 상태에서 logical block 100을 읽는다면 어떤일이 발생하나? 아무일도 없음. 왜냐하면 어디로 매핑 되어있는지 모르니까.
그래서 mapping table에 기록을 해야함.
요약하자면
쓸 공간을 찾고, 쓰고, logical to physical에 대한 정보를 쓰는 순서로 이뤄짐.

## Slide 25: A Log-Structured FTL (cont.)
Let’s now examine the rest of the writes in our example write stream
  101, 2000, and 2001. After writing these blocks, the state of the device is:
The log-based approach by its nature improves performance and greatly enhances reliability.
The FTL can now spread writes across all pages, performing what is called wear leveling and increasing the lifetime of the device
Unfortunately, this basic approach to log structuring has some downsides.
  The first is that overwrites of logical blocks lead to something we call garbage
    the device has to periodically perform garbage collection (GC)
  The second is high cost of in-memory mapping tables
DGIST
Notes: 이제 다음 예시를 들어보자.
101, 2000, 2001도 같은 순서로 작용함. log 구조로 FTL을 만드는 것은 성능과 신뢰도 면에서 다 좋은 향상을 이끌어냈음.
이제 골고루 분산됨으로써 wear levling이 수행되어 장치의 수명을 늘림.
하지만 이 방법도 단점들이 있는데, 여기서 덮어 쓰기가 수행될때는 더 이상 쓰이지 않을 contents들이 page상에 남아 있음. 이를 가비지라고 부르는데 이는 나중에 가비지 컬렉션이라는 작업을 함으로써 제거될 수 있음.
두번째는 메핑 테이블의 크기임.

## Slide 26: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 27: Garbage Collection
let’s assume that blocks 100 and 101 are written to again, with contents c1 and c2.
  The writes are written to the next free pages (in this case, physical pages 4 and 5)
  and the mapping table is updated accordingly.
Note that the device must have ﬁrst erased block 1 to make such programming possible:
The problem we have now should be obvious. physical pages 0 and 1, although marked VALID, have garbage in them
DGIST
Notes: 가장 먼저 가비지 컬렌션.
아까와 같은 상황인데 여기서 원하는건 logical 주소 100과 101이 가리키는 page의 contents를 c1과 c2로 수정하고 싶은 상황.
당연히 로그 구조에 의해 바로 다음 페이지는 4번과 5번에 각각 쓰면 됨.
물론 쓰기 전에 먼저 블록 1번을 지우고 씀.
이제 다 된거같지만 page 0과 page1은 우리가 더 이상 사용하지 않을 컨텐츠 인데도 여전히 유효하다고 되어있음. 이를 우리는 가비지라고 함.

## Slide 28: Garbage Collection (cont.)
The old versions of blocks 100 and 101. We call it garbage
The process of ﬁnding garbage blocks (also called dead blocks) and reclaiming them for future use is called Garbage Collection (GC)
The basic process of GC
  Find a block that contains one or more garbage pages
  Read in the live (non-garbage) pages from that block
  Write out those live pages to the log
  Finally reclaim the entire block for use in writing.
DGIST
Notes: 그래서 이제 GC 작업을 수행하여 이를 수거해감.
Gc의 순서는 우선 가비지 페이지가 있는 블록들을 찾고, 가비지가 아닌 live 페이지들을 읽음. 그리고 log 구조 방식으로 쓴 후에 가비지들을 수거해감.

## Slide 29: Garbage Collection (cont.)
Let’s now illustrate with an example.
  The device decides it wants to reclaim any dead pages within block 0 above.
  Block 0 has two dead blocks (pages 0 and 1) and two live blocks (pages 2 and 3, which contain blocks 2000 and 2001, respectively)
To do so
  Read live data (page 2,3) from block 0
  Write live data to end of the log
  Erase block 0 (freeing it for later usage)
  Can use the mapping table to determine whether each page within the block holds live data or not
DGIST
Notes: 이제 GC의 예시를 한번 보자..
아까 봤던 예시에 의하면 BLOCK 0은 두개의 데드블록 즉 page 0과 1을 가지고 있었고 2개의 live block page 2,3을 가지고 있었음.
이제 작업을 수행하기 위해서
Read live data, 그리고 이 data를 다음 로그에 쓴다.
그다음에 전체 블록을 지우고 메핑 테이블을 바꾸면 끝

## Slide 30: Garbage Collection (cont.)
Garbage collection can be expensive, requiring reading and rewriting of live data
  The ideal candidate for reclamation is a block that consists of only dead pages
    The block can immediately be erased and used for new data, without expensive data migration.
To reduce GC costs, some SSDs overprovision the device by adding extra ﬂash capacity, cleaning can be delayed and pushed to the background, perhaps done at a time when the device is less busy
  Adding more capacity also increases internal bandwidth, which can be used for cleaning and thus not harm perceived bandwidth to the client.
DGIST
Notes: GC는 매우 값비산 연산이다. 수거를 할때 있어서 가장 좋은 경우는 새로운 데이터를 바로 쓰고 값비산 연산이 필요도 없는 경우인데, 모든 페이지가 다 데드 블록인 경우다.
여튼 GC는 비싸다.
GC를 줄이기 위해서 우리는 OVERPROVISION이라는 것을 사용하는데, 이는 추가적은 연산 용량을 두고 직접 클리닝이 되는 시간을 지연시키는 것이다. 만약 우리가 작업을 몰아치고 있을때 GC까지 수행해야한다면 부하가 너무 크게 몰리게 된다.
하지만 여유 공간이 있다면 임시적으로 그걸 사용하고 향후에 여유가 있을때 GC 작업을 수행하면 되니 성능에 직접적인 영향을 줄 수 있다.

## Slide 31: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 32: Mapping Table Size
The second cost of log-structuring is the potential for extremely large mapping tables with one entry for each 4-KB page of the device
  With a large 1-TB SSD, a single 4-byte entry per 4-KB page results in 1GB of memory needed by the device
  Page-level FTL scheme is impractical
Block-Based Mapping
  Only keep a pointer per block of the device, instead of per page
  But using a block-based mapping inside a log-based FTL does not work very well for performance reasons.
  The biggest problem is “small write”; In this case, the FTL must read a large amount of live data from the old block and copy it into a new one
  So data copying increases write ampliﬁcation greatly and thus decreases performance.
DGIST
Notes: 두번째는 메핑 테이블 사이즈.
페이지 단위가 4kb라면 1TB의 SSD에서 1GB의 메모리가 메핑 테이블에 사용됨. 이는 문제있어보임
그래서 page-based mapping table이 아닌 block-based mapping table을 생각하게 됨.
말 그대로 page 단위로 포인터를 유지하는게 아니고 블록 단위로 포인터를 유지하는 것임.
하지만 이는 성능적인 문제로 인하여 잘 작동하지 않는데 가장 큰 문제는 small write 문제임. 이 문제가 반복되다보면 write amplification을 야기할 수 있음.

## Slide 33: Mapping Table Size (cont.)
Let’s look at an example
  Assume the client previously wrote out logical blocks 2000, 2001, 2002, and 2003 (with contents, a, b, c, d)
  they are located within physical block 1 at physical pages 4, 5, 6, and 7
With per-page mappings
  four mappings for these logical blocks: 2000→4, 2001→5, 2002→6, 2003→7
With block-level mapping
  a single address translation for all of this data.
  slightly different than our previous examples
  the logical block address consists of two portions: a chunk number and an offset.
DGIST
Notes: 이런 상황을 서로 비교해보자.
Page 단위일때는 이런 정도의 mapping table을 가져야하지만, block 단위 일때는 하나의 테이블 값만 가지면 된다. 이때 논리 블록 주소는 chunk 번호와 off set으로 구성된다.

## Slide 34: Mapping Table Size (cont.)
Let’s look at an example
  Logical blocks 2000, 2001, 2002, and 2003 all have the same chunk number (500)
  have different offsets (0, 1, 2, and 3, respectively)
In a block-based FTL, reading is easy
  First, the FTL extracts the chunk number from the logical block address by taking the top most bits out of the address
  Then, the FTL looks up the chunk number to physical-page mapping in the table
  Finally, the FTL computes the address of the desired flash page by adding the offset from the logical address to the physical address of the block.
DGIST
Notes: 가장 상위 비트에서 chunk 번호를 추출하고 여기에 offset을 더해 우리가 원하는 페이지 번호를 알 수 있음.

## Slide 35: Mapping Table Size (cont.)
For example : The client issues a read to logical address 2002
  Extracts the logical chunk number (500)
  Looks up the translation in the mapping table (finding 4)
  Adds the offset from the logical address (2) to the translation (4).
  Thre resulting physical-page address (6) is where the data is located
But what if the client writes to logical block 2002 with contents c’ ?
  In this case, the FTL must read in 2000, 2001, and 2003
  then write out all four logical blocks in a new location
  updating the mapping table accordingly
  Block 1 can be erased and reused, as shown here.
DGIST
Notes: 저 그림을 예로 든다면
우선 초기 mapping table이 가지고 있는 값인 4를 찾고 여기에 offse을 더함. 그러면 우리가 원하는 결과는 6이므로 여기에 원하는 값이 있음.
이제 문제는 새로운 내용으로 바꿀때임. 기본적으로 log 구조이기 때문에 이것들 모두 다 옮겨야함.
우리가 원하는거는 고작 하나의 컨텐츠만 옮기는것인데 4개의 page를 다 읽고 다 다시 써서 옮겨야함.

## Slide 36: Mapping Table Size (cont.)
Problem of Block level mappings
  Block level mappings greatly reduce the amount of memory needed for translations
  But cause significant performance problems when writes are smalller than the physical block size
Hybrid Mapping
  The FTL logically has two types of mapping table in its memory
  A small set of per-page mappings : log table, a larger set of per-block mappings : data table
  The FTL will ﬁrst consult the log table then will consult the data table to find its location and then access the requested data
The key to the hybrid mapping strategy; Keeping the number of log blocks small
  The FTL has to periodically examine log blocks and switch them into blocks that can be pointed to by only a single block pointer
  This switch is accomplished by one of three main techniques
DGIST
Notes: 이게 가장 큰 문제임.
그래서 우리는 하이브리드 매핑이라는 개념을 도입함.
두개의 매핑 테이블을 유지하게 되는데 page 단위로 기록하는 것이 log table, 블록 단위로 기록하는 것이 data table임.
여기서 핵심은 mapping table에 기록되지 않은 정보를 임시저장하는 log 블록을 최대한 적은 수로 유지하는 것이다.
FTL은 주기적으로 로그 블록들을 검사하고 하나의 블록 포인터로 유지해야함. 스위치 작업을 통해서 이를 수행한다.

## Slide 37: Mapping Table Size (cont.)
For example
  Previously written out logical pages 1000, 1001, 1002, and 1003 and placed them in physical block 2 (physical pages 8, 9, 10, 11)
  assume the contents of the writes to 1000, 1001, 1002, and 1003 are a, b, c, and d, respectively.
  Now assume that the client overwrites each of these blocks (with data a’, b’, c’, and d’) in physical block 0 (physical pages 0, 1, 2, and 3)
DGIST
Notes: 예를 들어서..
이런 경우에는 page 8,9,10,11에 있다고 가정. 논리적주소 1000,1001,1002,1003에 a,b,c,d가 있었고
이때 이 주소에 대응되는 컨텐츠들을 수정한다고 하자..
기존에는 log table은 없었지만 새로 페이지를 할당해서 사용해야하기 때문에 페이지에 대한 정보가 있어야하고 이를 매핑 테이블에 기입해야함.

## Slide 38: Mapping Table Size (cont.)
The FTL can perform what is known as a switch merge
This switch merge is the best case for a hybrid FTL.
Unfortunately, sometimes the FTL is not so lucky
DGIST
Notes: 이렇게 되면 이전에 있었던 블록2가 사라지고
이를 switch merge라고 부름

## Slide 39: Mapping Table Size (cont.)
Partial merge
  The FTL had to perform extra I/O to achieve its goals, thus increasing write ampliﬁcation.
Full merge
  Requires even more work
  The FTL must pull together pages from many other blocks to perform cleaning
  For example, imagine that logical blocks 0, 4, 8, and 12 are written to log block A
DGIST

## Slide 40: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 41: Page Mapping Plus Caching
Page Mapping Plus Caching
  Simpler ways to reduce the memory load of page-mapped FTLs
  Just to cache only the active parts of the FTL in memory
  The workload will display locality, and this caching approach will both reduce memory overheads and keep performance high.
DGIST

## Slide 42: Index
Introduction
Storing a Single Bit, From Bits to Banks/Planes
Basic Flash Operations
Flash Performance And Reliability
From Raw Flash to Flash-Based SSDs
FTL Organization: A Bad Approach
A Log-Structured FTL
Garbage Collection
Mapping Table Size
Page Mapping Plus Caching
Wear Leveling, SSD Performance And Cost
DGIST

## Slide 43: Wear Leveling
Wear leveling
  The basic log-structuring approach does a good initial job of spreading out write load, and garbage collection
  But sometimes, filled with long-lived data that does not get over-written
  FTL must periodically read all the live data out of such blocks and re-write it elsewhere, thus making the block available for writing again
  Simpler ways to reduce the memory load of page-mapped FTLs
  All blocks will wear out at roughly the same time, instead of a few “popular ” blocks quickly becoming unusable.
DGIST

## Slide 44: SSD Performance And Cost
Performance
Cost
  An SSD costs 60 cents per GB
  A typical hard drive costs 5 cents per GB.
DGIST